## Slide 1: ICTW Project Presentation Sanitizing (UV light) Remote Control Robot
Group Number: 38
Team Members:
Ansh Singh: IMT2020-013
Arun Singh Kushwaha: IMT2020-016
Lucky Kumar: IMT2020-051
Ritik Kumar: IMT2020-080
Submitted To: Dr. Somesh Kumar(Assistant Professor)

## Slide 2: Table of Contents
Motivation
Novelty
Sanitizing Remote Control Robot
Components Used
Connections and Coding
Miscellaneous
Applications in Real life
Future Improvements
Introduction

## Slide 3: Introduction
01.

## Slide 4
Motivation
The threat of the spread of the virus is not something new, but the recent COVID – 19 pandemic has caused many problems medically, socially, mentally and technologically.
The number of cases and deaths in INDIA due to COVID – 19, are increasing day by day, and to prevent his spread we must maintain utmost cleanliness.
So to do that we must disinfect the surface regularly but it is a tedious, time taking, risky process to disinfect the touched surface.
So with the thought of preventing further spread we came up with this idea of Sanitizing Remote Control Robot

## Slide 5: Introduction
The Sars-COV-2 is responsible for the disease known as COVID-19, which primarily spreads through contaminated surfaces. So to sanitize the surface is the most efficient way to minimize the spreading of COVID – 19. To ease the process of sanitizing, we have come up with the IDEA of SANITIZING RC ROBOT which uses UV light to sanitize a given area. It is faster, cost efficient, toxic free, environmental friendly unlike disinfectant liquids.
Notes: Novelty plis someone write it on your own

## Slide 6
02.
Sanitizing Remote Control Robot

## Slide 7: Our Sanitizing Robot is an autonomous robotic model that simply means that our robot have some sensors to detect the obstacle and environment. To make the robot autonomous we can use different kinds of sensor like radar, lidar, ultrasonic, IR modules . We choose IR modules because they are cheap and easy to interface with Arduino UNO . We are using UV led to sterilize the surfaces. This robot is very helpful as it is autonomous thus not man force is required to operate the robot. This help to break the chain of infection. The components used are very cheap and are easily available. Basically what our Robot does, it detects obstacle in surrounding and on UV led switch on in that direction and disinfects that area and automatically switches off after the sanitizing is completed. After that based on IR sensor input it turns in appropriate direction such that it doesn’t collide with the obstacles.

## Slide 8: Components Used I.

## Slide 9: Arduino Uno is a microcontroller board based on the ATmega328P. It has 14 digital input/output pins (of which 6 can be used as PWM outputs), 6 analog inputs, a 16 MHz ceramic resonator (CSTCE16M0V53-R0), a USB connection, a power jack, an ICSP header and a reset button. It contains everything needed to support the microcontroller; simply connect it to a computer with a USB cable or power it with a AC-to-DC adapter or battery to get started
Arduino Uno
Arduino Uno

## Slide 10: DC Motor
DC Motor is used for the movement of the Robot. We will use N20 DC Motor as it is light weight and capable of producing High Torque.
Motor Bracket
These motor bracket provide easy and secure mounting of the of the DC Motors in the project.
N20 DC Motor
Motor Brackets
Notes: Do Check the usage of the Motor Bracket Once

## Slide 11: The L293D is a popular 16-Pin Motor Driver IC. As the name suggests it is mainly used to drive motors. A single L293D IC is capable of running two DC Motors at the same time; also the direction of these two motors can be controlled independently. Using this L293D motor driver IC is very simple. The IC works on the principle of Half H-Bridge. H bridge is a set up which is used to run motors both in clock wise and anti clockwise direction.
Motor Driver
L293D Motor Driver Board

## Slide 12: Wheel
Wheel is required for the smooth movement of the robot on the surface.
Switch
The switch is used for the on / off the robot so that we can use remote to control the robot.
Wheel
Switch
Notes: Do Check the usage of the Motor Bracket Once

## Slide 13: An infrared (IR) sensor is an electronic device that measures and detects infrared radiation in its surrounding environment. IR is invisible to the human eye, as its wavelength is longer than that of visible light. Anything that emits heat gives off infrared radiation. Active infrared sensors both emit and detect infrared radiation. Active IR sensors have two parts: a light emitting diode (LED) and a receiver. When an object comes close to the sensor, The infrared light from the LED reflects off of the object and is detected by the receiver.
Infrared Sensor
Infrared Sensor

## Slide 14: UV Light LED
UV light is the most important component of our project. It is used to destroy the bacteria, viruses and parasites from the surfaces, room.
Lithium Ion Battery
Another important component of the Robot, without the battery we will not be able to operate the robot as a result we will not be able to sanitize the given place.
UV Light LED
Battery (7.42V)
Notes: Do Check the usage of the Motor Bracket Once

## Slide 15: What is UV light ?
Ultraviolet light is a type of electromagnetic radiation. Electromagnetic radiation comes from the sun and transmitted in waves or particles at different wavelengths and frequencies. This broad range of wavelengths is known as the electromagnetic (EM) spectrum. Ultraviolet (UV) light falls in the range of the EM spectrum between visible light and X-rays.
Why UV light ? ?
Bio-organisms such as bacteria, spores and viruses are known to be deactivated when exposed to UV-C light irradiation. UV light has been shown to destroy the RNA in viruses and can reduce the transmission of microbes, which can remain active on surfaces for long periods of time. Ultraviolet light destroys the genetic material in pathogens—DNA in bacteria and fungi, RNA in viruses—preventing them from reproducing.

## Slide 16: The HC-05 is a very cool module which can add two-way (full-duplex) wireless functionality to your projects. You can use this module to communicate between two microcontrollers like Arduino or communicate with any device with Bluetooth functionality like a Phone or Laptop. We can also configure the default values of the module by using the command mode. So if you looking for a Wireless module that could transfer data from your computer or mobile phone to microcontroller or vice versa then this module might be the right choice for you
HC-05 Bluetooth Module
HC-05 Bluetooth Module

## Slide 17: Connections And Coding
II.

## Slide 18: Why to Use Motor Driver IC ? ? Before getting answer of above question Let’s have a brief idea of working of motor. We need our robot to move in different direction. This can be done by changing the polarity of right and left motor. Thing to note here is motor move in anticlockwise direction when positive terminal is at high phase and negative is at low phase. Similarly motor move in clockwise direction when polarity are reverse. To change the polarity of the motor we are using a automatic system. To achieve this purpose we using a Arduino. But wait we have a problem, we can’t use Arduino directly to control motors.
Understanding Connections

## Slide 19
BUT WHY ??????????????????????
The reason is simple, we know Arduino output of is 5V But motor operate on 9V/12V. Thus Arduino can’t directly control motor as limited to work on 5V. HERE comes L293D motor diver IC in play. Basically what L293D does that it takes 5V signal from Arduino and accordingly provide 9V/12V power to motor and controls it. This make L293D IC prime component for every project dealing with motors. But how does this small IC is able to provide power to motor and controls it. To Know this we need look at the working of the IC.
L293D Motor Driver IC

## Slide 20: Connecting L293D IC
The L293D is a 16 pin IC, with eight pins, on each side, to controlling of two DC motor simultaneously. There are 4 INPUT pins, 4 OUTPUT pins and 2 ENABLE pin for each motor.
Connections with Arduino
1. Module 5V (VCC)(16) – Arduino 5V.
2. Module GND(13) – Arduino GND.
3. Input 1(2) – Arduino D2.
4.Output 1(3) – Motor Left ve.
5. Input 2(7) – Arduino D3.
6.Output 2(6) – Motor Left -ve
7. Input 3(15) – Arduino D4.
8.Output 3(14) – Motor Right +ve
9. Input4(10) – Arduino D5.
10.Output 4(11) – Motor Right -ve
11. Module VSS power terminal(8)- External power source of 9V.
12.Enable ½ (1) – D11
13.Enable ¾ (9) – D10

## Slide 22: Connecting the IR Sensor
Working
IR Sensor Module work in reverse logic that is it produce low signal when obstacle is present and high signal when obstacle is not present.
In the robot there are 3-IR Sensor, in left, right and forward direction. Each IR module has 3 pins Vcc , GND, Out. Vcc and GND of each IR sensor is connected to 5v and GND of Arduino respectively.
Out of each IR sensor is connected to different digital pins of Arduino.
Left IR Sensor –D6, Forward IR Sensor – D7, Right IR Sensor – D8

## Slide 23
Connecting Motors and LED
We have two motors each having two terminals positive and negative . They are connected to the IC . IC pins connection are shown in left side.
In the project we are using three UV Led, each for left, right and forward direction. When ever IR-Sensor detects an obstacle the respectively Led glows for 30 sec and disinfects the area.
LEFT Led – D9
RIGHT Led – D12
FORWARD Led – D13

## Slide 24: Connecting the Battery
The Battery Connections are very simple. The positive terminal of the battery is connected to Vss Motor Supply of IC pin 8.
The Negative terminal is connected to GND pin of Arduino

## Slide 25
Circuit Diagram

## Slide 26
HURRAY!!
Our circuit connection is completed
DESIGN LINK
Let’s Move to Coding Part

## Slide 27: Writing The Logic
Let’s first Define all the pins connected to Arduino
#define LEFT 6
#define FORWARD 7
#define RIGHT 8
#define LEFTLED 9
#define RIGHTLED 12
#define FORWARDLED 13
#define MOTORLEFTPOS 2
#define MOTORLEFTNEG 3
#define MOTORRIGHTPOS 4
#define MOTORRIGHTNEG 5
Every Components Connected to Arduino digital pins are defined above.

## Slide 28
Now Let’s define nature of each digital pins, whether the pin is input or output. This part is called void setup.
void setup()
{
pinMode(10, OUTPUT);
pinMode(11, OUTPUT);
pinMode(LEFT, INPUT);
pinMode(FORWARD, INPUT);
pinMode(RIGHT, INPUT);
pinMode(LEFTLED, OUTPUT);
pinMode(RIGHTLED, OUTPUT);
pinMode(LEFTLED, OUTPUT);
pinMode(MOTORLEFTPOS, OUTPUT);
pinMode(MOTORLEFTNEG, OUTPUT);
pinMode(MOTORRIGHTPOS, OUTPUT);
pinMode(MOTORRIGHTNEG, OUTPUT);
Serial.begin(9600);
}

## Slide 29
Now lets define condition for motor movements.
void softRight() {
digitalWrite(MOTORLEFTPOS, HIGH);
digitalWrite(MOTORLEFTNEG, LOW);
digitalWrite(MOTORRIGHTNEG, LOW);
digitalWrite(MOTORRIGHTPOS, LOW);
}
void stop(){
digitalWrite(MOTORLEFTPOS, LOW);
digitalWrite(MOTORLEFTNEG, LOW);
digitalWrite(MOTORRIGHTNEG, LOW);
digitalWrite(MOTORRIGHTPOS, LOW);
}
void turnLeft() {
digitalWrite(MOTORLEFTPOS, LOW);
digitalWrite(MOTORLEFTNEG, HIGH);
digitalWrite(MOTORRIGHTNEG, HIGH);
digitalWrite(MOTORRIGHTPOS, LOW);
}
void forward() {
digitalWrite(MOTORLEFTPOS, HIGH);
digitalWrite(MOTORLEFTNEG, LOW);
digitalWrite(MOTORRIGHTNEG, HIGH);
digitalWrite(MOTORRIGHTPOS, LOW);
}
void turnRight() {
digitalWrite(MOTORLEFTPOS, HIGH);
digitalWrite(MOTORLEFTNEG, LOW);
digitalWrite(MOTORRIGHTNEG, LOW);
digitalWrite(MOTORRIGHTPOS, HIGH);
}
void softLeft() {
digitalWrite(MOTORLEFTPOS, LOW);
digitalWrite(MOTORLEFTNEG, LOW);
digitalWrite(MOTORRIGHTNEG, HIGH);
digitalWrite(MOTORRIGHTPOS, LOW);
}

## Slide 30
Now Code the important part of the code that is loop function.
firstly lets switch the left and right part of the IC. We can use digital
write to set D10 and D11 to high voltage.
digitalWrite(10, HIGH);
digitalWrite(11, HIGH);
Now Take the reading of the IR sensor module using digital read .
bool a = digitalRead(LEFT);
bool b = digitalRead(RIGHT);
bool c = digitalRead(FORWARD);
Now switch on the Led based on above result. Like if obstacle is in left side
then Left IR sensor will have high value. So we can provide high value at left
led or pin D9 and then delay the robot for 30 sec so that it can sanitize
that area.
if(a==0){digitalWrite(LEFTLED,HIGH);stop();}
if(b==0){digitalWrite(RIGHTLED,HIGH);stop();}
if(c==0){digitalWrite(FORWARDLED,HIGH);stop();}
if(a==0||b==0||c==1)delay(30000);

## Slide 31
Now after our motor has sanitized the area we have to ensure that our robot doesn’t collide with the obstacle.
If obstacle is in left, left led switches on and after 30 sec we will call turnRight function to turn our robot to right. Using Permutation and Combination we have total 8 cases of the IR Sensor output.
if ((a==0)&&(c==1)&&(b==0)){forward(); Serial.println("Robo Moving Forward"); }
if ((a==1)&&(c==1)&&(b==1)){forward(); Serial.println("Robo Moving Forward");}
if ((a==0)&&(c==1)&&(b==1)){softRight();Serial.println("Robo Moving softRight"); }
if ((a==0)&&(c==0)&&(b==1)){turnRight(); Serial.println("Robo Moving Right"); }
if ((a==1)&&(c==1)&&(b==0)){softLeft(); Serial.println("Robo Moving softLeft");}
if ((a==1)&&(c==0)&&(b==0)){turnLeft(); Serial.println("Robo Moving Left"); }
if ((a==1)&&(c==0)&&(b==1)){turnLeft(); Serial.println("Robo Moving Left"); }
if ((a==0)&&(c==0)&&(b==0)){turnLeft(); Serial.println("Robo Moving Left");}

## Slide 32
We Are Finished With Coding Part …….
https://github.com/arun-kushwaha04/ICTW/tree/main/Code/Logic.txt

## Slide 33
Miscellaneous
03.

## Slide 34: Applications in Real Life
One-time cost (No need to refill alcohol or chlorine liquid).
Can be used to disinfect surfaces, medical suits, medical masks, and other medical equipment.
Reduce the disinfection time by 60% when compared to liquid-based disinfection methods.
Ability to use for environments with electronic equipment.
One operator can cover a large area.
It has been proven by many institute that the disinfection rate of this type of robot is 99.9997% of germs and it is also capable of killing CORONA VIRUS

## Slide 35
Improvement
04.

## Slide 36: Applications in Real Life
As we know Uv rays are harmful for humans. Our robot will treat human same as obstacles and therefore sanitize them. To prevent this we can add PIR sensor that will detect any human movement and on detection on human movement we can switch off the LED’s.
We are planning to add remote operation to our robot .Our robot is fully autonomous there are chances that It can’t sanitize a surface or we personally want to sanitize a particular surface. To achieve this functionality we can use the HC-05 Bluetooth module.

## Slide 37: Resources